How to add an (S)VGA driver to XFree86
  Copyright (c) 1993, 1994 David E. Wexelblat <dwex@XFree86.org>
  Issue 1.3 - May 29, 1994

  1.  Introduction

  Adding support for a new SVGA chipset to XFree86 is a challenging
  project for someone who wants to learn more about hardware-level
  programming.  It can be fraught with hazards (in particular, crashing
  the machine is all too common).  But in the end, when the server comes
  up and functions, it is immensely satisfying.

  Adding support for an SVGA chipset does not change any of the basic
  functioning of the server.  It is still a dumb 8-bit PseudoColor
  server or 1-bit StaticGray server.  Adding support for new hardware
  (e.g. accelerated chips) is a major undertaking, and is not anywhere
  near formalized enough yet that it can be documented.

  Nonetheless, the driver-level programming here is a good introduction.
  And can well be the first step for adding support for an accelerated
  chipset, as many are SVGA-supersets.  Writing an SVGA-level driver for
  the chipset can provide a stable development platform for making use
  of new features (in fact, this has been done for the S3, Cirrus, and
  WD accelerated chipsets, for internal use as the accelerated servers
  are developed for XFree86 2.0).

  Now let's get down to it.  In addition to this documentation, a stub
  driver has been provided.  This should provide you a complete
  framework for your new driver.  Don't let the size of this document
  persuade you that this is an overly difficult task.  A lot of work has
  been put into making this document as close to complete as possible;
  hence it should, in theory, be possible to use this as a cookbook, and
  come out with a working driver when you reach the end.  I do advise
  that you read it all the way through before starting.


  2.  Getting Started

  The first step in developing a new driver is to get the documentation
  for your chipset.  I've included a list of vendor contact information
  that I have collected so far (it's far from complete, so if you have
  any that isn't on the list, please send it to me).  You need to obtain
  the databook for the chipset.  Make sure that the person you speak to
  is aware that you intend to do register-level programming (so they
  don't send you the EE-style datasheet).  Ask for any example code, or
  developer's kits, etc.  I've learned that at the SVGA level, in
  general, a databook that lists and describes the registers is the most
  you can hope to find.

  If you are not familiar with VGA register-level programming, you
  should get (and read!) a copy of Richard Ferraro's bible (see
  references below).  The best way to understand what is happening in
  the server is to study the workings of the monochrome server's
  ``generic'' server, and compare it with the documentation in Ferraro's
  book (be aware that there are a few errors in the book).  You can find
  the generic-VGA-register handling functions in the file ``vgaHW.c''.

  Once you understand what's happening in the generic server, you should
  study one or more of the existing SVGA drivers.  Obtain the databook
  for a supported SVGA chipset, and study the documentation along with
  the code.  When you have a good understanding of what that driver does
  over and above the generic VGA, you will know what information you
  need to obtain from the databook for the new chipset.  Once you have
  this information, you are ready to begin work on your new driver.


  3.  Directory Tree Structure

  Here is an outline of the directory tree structure for the source
  tree.  Only directories/files that are relevant to writing a driver
  are presented.  The structure for the Link Kit is presented below.


     xc/config/cf/

        site.def
           Local configuration customization

        xf86site.def
           XFree86 local configuration customization


     xc/programs/Xserver/hw/xfree86/
        The server source

        common/
           Files common to all of the server (XF86Config parser, I/O
           device handlers, etc)

           xf86.h
              Contains the `ScrnInfoRec' data structure

           xf86_Option.h
              Contains option flags

           compiler.h
              Contains in-line assembler macros and utility functions

        os-support/
           OS-support layer

           assyntax.h
              Contains macro-ized assembler mnemonics

           xf86_OSlib.h
              OS-support includes, defines, and prototypes

        LinkKit/

           site.def.LK
              Template for Link Kit site.def

        vga256/
           256-color VGA server directories

           vga/
              The generic VGA handling code

              vga.h
                 Contains the `vgaVideoChipRec' and `vgaHWRec' data
                 structures

              vgaHW.c
                 Contains the generic-VGA-register handling functions
                 vgaHWInit(), vgaHWSave() and vgaHWRestore().

           drivers/
              Contains the SVGA driver subdirectories.  Each contains an
              Imakefile, a .c file for the driver, and a .s file for the
              bank- switching functions.


        vga2/
           The monochrome vga server directories.  Most of the files are
           linked from vga256, and the differences handled by
           conditional compilation.

           drivers/
              The SVGA driver subdirectories.  The `generic' VGA driver
              is also located here.

        vga16/
           The 16-color vga server directories.  Most of the files are
           linked from vga256, and the differences handled by
           conditional compilation.

           drivers/
              The SVGA driver subdirectories.

        VGADriverDoc/
           This documentation and the stub driver.

  The Link Kit is usually installed in /usr/X11R6/lib/Server.  The Link
  Kit contains everything that is needed to relink the server.  It is
  possible to write a new driver and build a new server without having
  even the server source installed.

     Server/

        site.def
           Local configuration customization

        include/
           All of the include files listed under the `common' directory
           above

        drivers/
           All of the SVGA drivers

           vga2/
              The SVGA driver subdirectories.

           vga16/
              The SVGA driver subdirectories.

           vga256/
              The SVGA driver subdirectories.

        VGADriverDoc/
           The directory with this documentation and the stub driver.
           `vgaHW.c' is also copied here, for reference (it is not built
           as part of the Link Kit).


  4.  Setting Up The Build Information

  This section describes the peripheral configuration and build steps
  that must be performed to set up for your new driver.  The steps are
  the same whether you are building from the source tree of from the
  Link Kit; only the locations of the files is different.  Here are the
  configuration steps that must be followed:


     1. Choose the name for your driver subdirectory and data
        structures.  Since the current driver scheme allows (in fact,
        encourages) putting drivers for multiple related chipsets in a
        single driver, it is usually best to use the vendor name, rather
        than a chipset version.  The fact that older XFree86 drivers do
        not follow this convention should not deter you from using it
        now - most of that code was developed before the driver
        interface had been made flexible and extensible.

        For this documentation, we'll use chips from the SuperDuper
        Chips vendor.  Hence, we'll use `sdc' for the name of the
        driver.

     2. Decide whether your driver will support the color server, the
        monochrome server, or both.  For this documentation, we will
        assume that both the color and monochrome servers will be
        supported.  If you intend to support only the color server, the
        steps for the monochrome server can be ignored.  If you intend
        to support only the monochrome server, the steps for the color
        server listed should be performed for the monochrome server, and
        the monochrome steps ignored.  Most of the existing drivers
        support only the color or both servers; the ``generic'' driver
        is the only driver (currently) that supports just the monochrome
        server.

     3. Create your driver directories:


        o  If you are working in the source tree, create the following
           directories:

              xc/programs/Xserver/hw/xfree86/vga256/drivers/sdc
              xc/programs/Xserver/hw/xfree86/vga16/drivers/sdc
              xc/programs/Xserver/hw/xfree86/vga2/drivers/sdc


        o  If you are working in the Link Kit, create the following
           directories:

              /usr/X11R6/lib/Server/drivers/vga256/sdc
              /usr/X11R6/lib/Server/drivers/vga16/sdc
              /usr/X11R6/lib/Server/drivers/vga2/sdc



     4. Set up the Imakefile parameters to cause your driver to be
        built:


        o  If you are working in the source tree:

           a. Edit the file xc/config/cf/xfree86.cf, and add `sdc' to
              the list for the definitions for `XF86Vga256Drivers',
              `XF86Vga16Drivers' and `XF86Vga2Drivers'.  You should put
              `sdc' just before `generic' in the list (i.e. second
              last), to ensure that none of the other driver's probe
              functions incorrectly detect the `sdc' chipset .

           b. Edit the file xc/config/cf/xf86site.def, and add the same
              entries in this file (this is just a comment that shows
              the default values).

           c. Edit the site.def.LK file in
              xc/programs/Xserver/hw/xfree86/LinkKit/, and add the same
              entries in this file.  This is the prototype `site.def'
              file that will be installed in the Link Kit.



        o  If you are working in the Link Kit, edit the file
           /usr/X11R6/lib/Server/site.def, and add `sdc' to the
           `XF86Vga256Drivers', `XF86Vga16Drivers' and `XF86Vga2Drivers'
           definitions as described in (a) above.

     5. Now copy the prototype files into your new directories:

        o  If you are working in the source tree, copy the `stub' files
           as follows (directories are below xc/programs/Xserver):

           Imakefile.stub =>
              hw/xfree86/vga256/drivers/sdc/Imakefile

           stub_driver.c =>
              hw/xfree86/vga256/drivers/sdc/sdc_driver.c

           stub_bank.s =>
              hw/xfree86/vga256/drivers/sdc/sdc_bank.s

           Imakefile.stub =>
              hw/xfree86/vga16/drivers/sdc/Imakefile (then edit this
              Imakefile and make the changes described in the comments).

           Imakefile.stub =>
              hw/xfree86/vga2/drivers/sdc/Imakefile (then edit this
              Imakefile and make the changes described in the comments).

        o  If you are working in the Link Kit, copy the `stub' files as
           follows:

           Imakefile.stub =>
              /usr/X11R6/lib/Server/drivers/vga256/sdc/Imakefile

           stub_driver.c =>
              /usr/X11R6/lib/Server/drivers/vga256/sdc/sdc_driver.c

           stub_bank.s =>
              /usr/X11R6/lib/Server/drivers/vga256/sdc/sdc_bank.s

           Imakefile.stub =>
              /usr/X11R6/lib/Server/drivers/vga16/sdc/Imakefile (then
              edit this Imakefile and make the changes described in the
              comments).

           Imakefile.stub =>
              /usr/X11R6/lib/Server/drivers/vga2/sdc/Imakefile (then
              edit this Imakefile and make the changes described in the
              comments).

     6. Edit each of the files you've just copied, and replace `stub'
        with `sdc' and `STUB' with `SDC' wherever they appear.

  That's all the prep work needed.  Now it's time to work on the actual
  driver.


  5.  The Bank-Switching Functions

  The normal VGA memory map is 64k starting at address 0xA0000.  To
  access more than 64k of memory, SuperVGA chipsets implement ``bank
  switching'' - the high-order address bits are used to select the bank
  of memory in which operations will take place.  The size and number of
  these banks varies, and will be spelled out in the chipset
  documentation.  A chipset will have zero, one or two bank registers.
  Likely the ONLY case of zero bank registers is a generic VGA, and
  hence is not a concern.

  Note that some of the newer chipsets (e.g. Trident 8900CL, Cirrus)
  allow for a linear mapping of the video memory.  While using such a
  scheme would improve the performance of the server, it is not
  currently supported.  Hence there is no way to use such features for a
  new chipset.

  Most SVGA chipsets have two bank registers.  This is the most
  desirable structure (if any banking structure can be called
  ``desirable''), because data can be moved from one area of the screen
  to another with a simple `mov' instruction.  There are two forms of
  dual-banking - one where the two bank operations define a read-only
  bank and a write-only bank, and one with two read/write windows.  With
  the first form, the entire SVGA memory window is used for both read a
  write operations, and the two bank registers determine which bank is
  actually used (e.g. ET3000, ET4000).  With the second form, the SVGA
  memory window is split into two read/write banks, with each bank
  pointer being used to control one window.  In this case, one window is
  used for read operations and the other for write operations (e.g.
  PVGA1/Western Digital, Cirrus).

  A chipset that has a single bank register uses that one bank for both
  read and write access.  This is problematic, because copying
  information from one part of the screen to another requires that the
  data be read in, stored, and then written out.  Fortunately, the
  server is able to handle both one-bank and two-bank chipsets; the
  determination of behavior is defined by an entry in the driver data
  structure described below.

  A driver requires that three assembly-language functions be written,
  in the file `sdc_bank.s'.  These functions set the read bank -
  SDCSetRead(), the write bank - SDCSetWrite(), and set both banks -
  SDCSetReadWrite().  For a chipset with only one bank, all three will
  be declared as entry points to the same function (see the ``tvga8900''
  driver for an example).

  The functions are fairly simple - the bank number is passed to the
  function in register %al.  The function will shift, bitmask, etc -
  whatever is required to put the bank number into the correct form -
  and then write it to the correct I/O port.  For chipsets where the two
  banks are read-only HERE and write-only, the SetReadWrite() function
  will have to do this twice - once for each bank.  For chipsets with
  two independent read/write windows, the SetReadWrite() function should
  use the same bank as the SetWrite() function.

  A special note - these functions MUST be written in the macroized
  assembler format defined in the header file ``assyntax.h''.  This will
  ensure that the correct assembler code will be generated, regardless
  of OS.  This macroized format currently supports USL, GNU, and Intel
  assembler formats.

  That's all there is to the banking functions.  Usually the chipset
  reference will give examples of this code; if not, it is not difficult
  to figure out, especially using the other drivers as examples.


  6.  The Driver Itself

  Now it's time to get down to the real work - writing the major driver
  functions in the files sdc_driver.c.  First, an overview of what the
  responsibilities of the driver are:


     1. Provide a chipset-descriptor data structure to the server.  This
        data structure contains pointers to the driver functions and
        some data-structure initialization as well.


     2. Provide a driver-local data structure to hold the contents of
        the chipset registers.  This data structure will contain a
        generic part and a driver-specific part.  It is used to save the
        initial chipset state, and is initialized by the driver to put
        the chipset into different modes.

     3. Provide an identification function that the server will call to
        list the chipsets that the driver is capable of supporting.

     4. Provide a probe function that will identify this chipset as
        different from all others, and return a positive response if the
        chipset this driver supports is installed, and a negative
        response otherwise.

     5. Provide a function to select dot-clocks available on the board.

     6. Provide functions to save, restore, and initialize the driver-
        local data structure.

     7. Provide a function to set the starting address for display in
        the video memory.  This implements the virtual-screen for the
        server.

     8. Perhaps provide a function for use during VT-switching.

     9. Perhaps provide a function to check if each mode is suitable for
        the chipset being used.

  Before stepping through the driver file in detail, here are some
  important issues:


     1. If your driver supports both the color and monochrome servers,
        you should take care of both cases in the same file.  Most
        things are the same - you can differentiate between the two with
        the MONOVGA #define.  If the 16 color server is supported, code
        specific to it can be enabled with the XF86VGA16 #define.  In
        most cases  it is sufficient to put the following near the top
        of the stub_driver.c file:

           #ifdef XF86VGA16
           #define MONOVGA
           #endif


     2. The color server uses the SVGA's 8-bit packed-pixel mode.  The
        monochrome and vga16 servers uses the VGA's 16-color mode (4
        bit-planes).  Only one plane is enabled for the monochrome
        server.

     3. It is possible for you to define your monochrome driver so that
        no bank-switching is done.  This is not particularly desirable,
        as it yields only 64k of viewing area.

  Keeping these things in mind, you need to find the registers from your
  SVGA chipset that control the desired features.  In particular, regis-
  ters that control:

     1. Clock select bits.  The two low-order bits are part of the
        standard Miscellaneous Output Register; most SVGA chipsets will
        include 1 or 2 more bits, allowing the use of 8 or 16 discrete
        clocks.

     2. Bank selection.  The SVGA chipset will have one or two registers
        that control read/write bank selection.

     3. CRTC extensions.  The standard VGA registers don't have enough
        bits to address large displays.  So the SVGA chipsets have
        extension bits.

     4. Interlaced mode.  Standard VGA does not support interlaced
        displays.  So the SVGA chipset will have a bit somewhere to
        control interlaced mode.  Some chipsets require additional
        registers to be set up to control interlaced mode

     5. Starting address.  The standard VGA only has 16 bits in which to
        specify the starting address for the display.  This restricts
        the screen size usable by the virtual screen feature.  The SVGA
        chipset will usually provide one or more extension bits.

     6. Lock registers.  Many SVGA chipset prevent modification of
        extended registers unless the registers are first ``unlocked''.
        You will need to disable protection of any registers you will
        need for other purposes.

     7. Any other facilities.  Some chipset may, for example, require
        that certain bits be set before you can access extended VGA
        memory (beyond the IBM-standard 256k).  Or other facilities;
        read through all of the extended register descriptions and see
        if anything important leaps out at you.

  If you are fortunate, the chipset vendor will include in the databook
  some tables of register settings for various BIOS modes.  You can
  learn a lot about what manipulations you must do by looking at the
  various BIOS modes.


  6.1.  Multiple Chipsets And Options

  It is possible, and in fact desirable, to have a single driver support
  multiple chipsets from the same vendor.  If there are multiple
  supported chipsets, then you would have a series of #define's for
  them, and a variable `SDCchipset', which would be used throughout the
  driver when distinctions must be made.  See the Trident and PVGA1/WD
  drivers for examples (the Tseng ET3000 and ET4000 are counter-examples
  - these were implemented before the driver interface allowed for
  multiple chipsets, so this example should NOT be followed).  Note that
  you should only distinguish versions when your driver needs to do
  things differently for them.  For example, suppose the SDC driver
  supports the SDC-1a, SDC-1b, and SDC-2 chipsets.  The -1a and -1b are
  essentially the same, but different from the -2 chipset.  Your driver
  should support the -1 and -2 chipsets, and not distinguish between the
  -1a and -1a.  This will simplify things for the end user.

  In cases where you want to give the user control of driver behavior,
  or there are things that cannot be determined without user
  intervention, you should use ``option'' flags.  Say that board vendors
  that use the SDC chipsets have the option of providing 8 or 16 clocks.
  There's no way you can determine this from the chipset probe, so you
  provide an option flag to let the user select the behavior from the
  XF86Config file.  The option flags are defined in the file
  ``xf86_option.h''.  You should look to see if there is already a flag
  that can be reused.  If so, use it in your driver.  If not, add a new
  #define, and define the string->symbol mapping in the table in that
  file.  To see how option flags are used, look at the ET4000, PVGA1/WD,
  and Trident drivers.


  6.2.  Data Structures

  Once you have an understanding of what is needed from the above
  description, it is time to fill in the driver data structures.  First
  we will deal with the `vgaSDCRec' structure.  This data structure is
  the driver-local structure that holds the SVGA state information.  The
  first entry in this data structure is ALWAYS `vgaHWRec std'.  This
  piece holds the generic VGA portion of the information.  After that,
  you will have one `unsigned char' field for each register that will be
  manipulated by your driver.  That's all there is to this data
  structure.

  Next you must initialize the `SDC' structure (type `vgaVideoChipRec').
  This is the global structure that identifies your driver to the
  server.  Its name MUST be `SDC', in all caps - i.e. it must match the
  directory name for your driver.  This is required so that the Link Kit
  reconfiguration can identify all of the requisite directories and
  global data structures.

  The first section of this structure simply holds pointers to the
  driver functions.

  Next, you must initialize the information about how your chipset does
  bank switching.  The following fields must be filled in:

     1. ChipMapSize - the amount of memory that must be mapped into the
        server's address space.  This is almost always 64k (from 0xA0000
        to 0xAFFFF).  Some chipsets use a 128k map (from 0xA0000 to
        0xBFFFF).  If your chipset gives an option, use the 64k window,
        as a 128k window rules out using a Hercules or Monochrome
        Display Adapter card with the SVGA.

     2. ChipSegmentSize - the size of each bank within the ChipMapSize
        window.  This is usually also 64k, however, some chipsets split
        the mapped window into a read portion and a write portion (for
        example the PVGA1/Western Digital chipsets).

     3. ChipSegmentShift - the number of bits by which an address will
        be shifted right to mask of the bank number.  This is log-base-2
        of ChipSegmentSize.

     4. ChipSegmentMask - a bitmask used to mask off the address within
        a given bank.  This is (ChipSegmentSize-1).

     5. ChipReadBottom,ChipReadTop - the addresses within the mapped
        window in which read operations can be done.  Usually 0, and
        64k, respectively, except for those chipset that have separate
        read and write windows.

     6. ChipWriteBottom,ChipWriteTop - same as above, for write
        operations.

     7. ChipUse2Banks - a boolean value for whether this chipset has one
        or two bank registers.  This is used to set up the screen-to-
        screen operations properly.

  There are three more fields that must be filled in:

     1. ChipInterlaceType - this is either VGA_NO_DIVIDE_VERT or
        VGA_DIVIDE_VERT.  Some chipsets require that the vertical timing
        numbers be divided in half for interlaced modes.  Setting this
        flag will take care of that.

     2. ChipOptionFlags - this should always be `{0,}' in the data
        structure initialization.  This is a bitfield that contains the
        Option flags that are valid for this driver.  The appropriate
        bits are initialized at the end of the Probe function.

     3. ChipRounding - this gets set to the multiple by which the
        virtual width of the display must be rounded for the 256-color
        server.  This value is usually 8, but may be 4 or 16 for some
        chipsets.


  6.3.  The Ident() function

  The Ident() function is a very simple function.  The server will call
  this function repeatedly, until a NULL is returned, when printing out
  the list of configured drivers.  The Ident() function should return a
  chipset name for a supported chipset.  The function is passed a number
  which increments from 0 on each iteration.


  6.4.  The ClockSelect() function

  The ClockSelect() function is used during clock probing (i.e. when no
  `Clocks' line is specified in the XF86Config file) to select the dot-
  clock indicated by the number passed in the parameter.  The function
  should set the chipset's clock-select bits according to the passed-in
  number.  Two dummy values will be passed in as well (CLK_REG_SAVE,
  CLK_SAVE_RESTORE).  When CLK_REG_SAVE is passed, the function should
  save away copies of any registers that will be modified during clock
  selection.  When CLK_REG_RESTORE is passed, the function should
  restore these registers.  This ensure that the clock-probing cannot
  corrupt registers.

  This function should return FALSE if the passed-in index value is
  invalid or if the clock can't be set for some reason.


  6.5.  The Probe() function

  The Probe() function is perhaps the most important, and perhaps the
  least intuitive function in the driver.  The Probe function is
  required to identify the chipset independent of all other chipsets.
  If the user has specified a `Chipset' line in the XF86Config file,
  this is a simple string comparison check.  Otherwise, you must use
  some other technique to figure out what chipset is installed.  If you
  are lucky, the chipset will have an identification mechanism
  (ident/version registers, etc), and this will be documented in the
  databook.  Otherwise, you will have to determine some scheme, using
  the reference materials listed below.

  The identification is often done by looking for particular patterns in
  register, or for the existence of certain extended registers.  Or with
  some boards/chipsets, the requisite information can be obtained by
  reading the BIOS for certain signature strings.  The best advise is to
  study the existing probe functions, and use the reference
  documentation.  You must be certain that your probe is non-destructive
  - if you modify a register, it must be saved before, and restored
  after.

  Once the chipset is successfully identified, the Probe() function must
  do some other initializations:

     1. If the user has not specified the `VideoRam' parameter in the
        XF86Config file, the amount of installed memory must be
        determined.

     2. If the user has not specified the `Clocks' parameter in the
        XF86Config file, the values for the available dot-clocks must be
        determined.  This is done by calling the vgaGetClocks()
        function, and passing it the number of clocks available and a
        pointer to the ClockSelect() function.


     3. It is recommended that the `maxClock' field of the server's
        `vga256InfoRec' structure be filled in with the maximum dot-
        clock rate allowed for this chipset (specified in KHz).  If this
        is not filled in a probe time, a default (currently 90MHz) will
        be used.

     4. The `chipset' field of the server's `vga256InfoRec' structure
        must be initialized to the name of the installed chipset.

     5. If the driver will be used with the monochrome server, the
        `bankedMono' field of the server's `vga256InfoRec' structure
        must be set to indicate whether the monochrome driver supports
        banking.

     6. If any option flags are used by this driver, the
        `ChipOptionFlags' structure in the `vgaVideoChipRec' must be
        initialized with the allowed option flags using the OFLG_SET()
        macro.


  6.6.  The EnterLeave() function

  The EnterLeave() function is called whenever the virtual console on
  which the server runs is entered or left (for OSs without virtual
  consoles, the function is called when the server starts and again when
  it exits).  The purpose of this function is to enable and disable I/O
  permissions (for OSs where such is required), and to unlock and relock
  access to ``protected'' registers that the driver must manipulate.  It
  is a fairly trivial function, and can be implemented by following the
  comments in the stub driver.


  6.7.  The Restore() function

  The Restore() function is used for restoring a saved video state.
  Note that `restore' is a bit of a misnomer - this function is used to
  both restore a saved state and to install a new one created by the
  server.  The Restore() function must complete the following actions:

     1. Ensure that Bank 0 is selected, and that any other state
        information required prior to writing out a new state has been
        set up.

     2. Call vgaHWRestore() to restore the generic VGA portion of the
        state information.  This function is in the vgaHW.c file.

     3. Restore the chipset-specific portion of the state information.
        This may be done by simply writing out the register, or by doing
        a read/modify/write cycle if only certain bits are to be
        modified.  Be sure to note the comment in the sample driver
        about how to handle clock-select bits.

  6.8.  The Save() function

  The Save() function is used to extract the initial video state
  information when the server starts.  The Save() function must complete
  the following actions:

     1. Ensure that Bank 0 is selected.

     2. Call vgaHWSave() to extract the generic VGA portion of the state
        information.  This function is in the vgaHW.c file.

     3. Extract the chipset-specific portion of the state information.


  6.9.  The Init() function

  The Init() function is the second most important function in the
  driver (after the Probe() function).  It is used to initialize a data
  structure for each of the defined display modes in the server.  This
  function is required to initialize the entire `vgaSDCRec' data
  structure with the information needed to put the SVGA chipset into the
  required state.  The generic VGA portion of the structure is
  initialized with a call to vgaHWInit() (also located in vgaHW.c).

  Once the generic portion is initialized, the Init() function can
  override any of the generic register initialization, if necessary.
  All of the other fields are filled in with the correct initialization.
  The information about the particular mode being initialized is passed
  in the `mode' parameter, a pointer to a `DisplayModeRec' structure.
  This can be dereferenced to determine the needed parameters.

  If you only know how to initialize certain bits of the register, do
  that here, and make sure that the Restore() function does a
  read/modify/write to only manipulate those bits.  Again, refer to the
  existing drivers for examples of what happens in this function.


  6.10.  The Adjust() function

  The Adjust() function is another fairly basic function.  It is called
  whenever the server needs to adjust the start of the displayed part of
  the video memory, due to scrolling of the virtual screen or when
  changing the displayed resolution.  All it does is set the starting
  address on the chipset to match the specified coordinate.  Follow the
  comments in the stub driver for details on how to implement it.


  6.11.  The ValidMode() function

  The ValidMode() function is required.  It is used to check for any
  chipset-dependent reasons why a graphics mode might not be valid.  It
  gets called by higher levels of the code after the Probe() stage.  In
  many cases no special checking will be required and this function will
  simply return TRUE always.


  6.12.  The SaveScreen() function

  The SaveScreen() function is not needed by most chipsets.  This
  function would only be required if the extended registers that your
  driver needs will be modified when a synchronous reset is performed on
  the SVGA chipset (your databook should tell you this).  If you do NOT
  need this function, simply don't define it, and put `NoopDDA' in its
  place in the vgaVideoChipRec structure initialization (NoopDDA is a
  generic-use empty function).

  If you DO need this function, it is fairly simple to do.  It will be
  called twice - once before the reset, and again after.  It will be
  passed a parameter of SS_START in the former case, and SS_FINISH in
  the latter.  All that needs to be done is to save any registers that
  will be affected by the reset into static variables on the SS_START
  call, and then restore them on the SS_FINISH call.


  6.13.  The GetMode() function

  The GetMode() function is not used as of XFree86 1.3; its place in the
  vgaVideoChipRec should be initialized to `NoopDDA'.

  At some point in the future, this function will be used to enable the
  server and/or a standalone program using the server's driver libraries
  to do interactive video mode adjustments.  This function will read the
  SVGA registers and fill in a DisplayModeRec structure with the current
  video mode.


  6.14.  The FbInit() function

  The FbInit() function is required for drivers with accelerated
  graphics support.  It is used to replace default cfb.banked functions
  with accelerated chip-specific versions.  vga256LowlevFuncs is a
  struct containing a list of functions which can be replaced.  This
  struct defined in vga256.h.  Examples of FbInit() functions can be
  found in the et4000, pvga1 and cirrus drivers.

  If you do NOT need this function, simply don't define it, and put
  `NoopDDA' in its place in the vgaVideoChipRec structure
  initialization.


  7.  Building The New Server

  As in the setup work, the steps for building the server depend whether
  you are working in the source tree or in the Link Kit.  Here are the
  steps for the initial build after installing your new driver files:

     o  If you are working in the source tree, follow these steps:

        Go to xc/programs/Xserver, and enter `make Makefile', then `make
        Makefiles depend all'

     o  If you are working in the Link Kit, follow these steps:


        1. Go to /usr/X11R6/lib/Server, and enter `./mkmf'

        2. In the same directory, enter `make'

  To rebuild the server after the initial build (e.g. after making
  changes to your driver):


     o  If you are working in the source tree, follow these steps:


        1. Go to the appropriate drivers/ directory (e.g.,
           xc/programs/Xserver/hw/xfree86/vga256/drivers), and enter
           `make'.

        2. Go to xc/programs/Xserver, and enter `make loadXF86_SVGA' (to
           link the color server), `make loadXF86_VGA16' (to link the 16
           color server) or `make loadXF86_Mono' (to link the mono
           server).


     o  If you are working in the Link Kit, follow these steps:


        1. Go to the appropriate driver directory, and enter `make'.

        2. Go to /usr/X11R6/lib/server, and enter `make loadXF86_SVGA'
           (to link the color server) or `make loadXF86_VGA16' (to link
           the 16 color server) or `make loadXF86_Mono' (to link the
           mono server).


  8.  Debugging

  Debugging a new driver can be a painful experience, unfortunately.  It
  is likely that incorrect programming of the SVGA chipset can lock up
  your machine.  More likely, however, is that the display will be lost,
  potentially requiring a reboot to correct.  It is HIGHLY recommended
  that the server be run from an attached terminal or a network login.
  This is the only rational way in which a debugger can be used on the
  server.  Attempting to use multiple VTs for debugging is basically a
  waste of time.

  Because of the potential for locking up the machine, it is a VERY good
  idea to remember to do a `sync' or two before starting the server.  In
  addition, any unnecessary filesystems should be unmounted while the
  debugging session is going on (to avoid having to run unnecessary
  fsck's).

  By default the server is built without debugging symbols.  The server
  can grow VERY large with debugging enabled.  It is very simple to
  rebuild your driver for debugging, though.  Do the following:


     1. Go to the driver directory.

     2. Edit the Makefile.  Look for the SECOND definition of
        `CDEBUGFLAGS'.  Change this definition to

                        CDEBUGFLAGS = -g -DNO_INLINE



     (this will enable debugging symbols and disable inlining of func-
     tions, which can make single-stepping a nightmare).

     3. Remove the `sdc_driver.o' file.

     4. Now follow the steps above for rebuilding the server.

        (Alternatively, instead of editing the Makefile, you can simply
        do `make CDEBUGFLAGS="-g -DNO_INLINE"' after removing the old .o
        file, then rebuild the server as described above).

  This will give you a server with which you can set breakpoints in the
  driver functions and single-step them.  If you are working in the
  source tree, and just learning about SVGA programming, it may be
  useful to rebuild vgaHW.c with debugging as well.


  9.  Advice

  I cannot stress this enough - study all available references, and the
  existing code, until you understand what is happening.  Do this BEFORE
  you begin writing a driver.  This will save you a massive amount of
  headache.  Try to find a driver for a chipset that is similar to
  yours, if possible.  Use this as an example, and perhaps derive your
  driver from it.

  Do not let the gloom-and-doom in the debugging section  discourage
  you.  While you will probably have problems initially (I still do),
  careful, deliberate debugging steps can bear fruit very quickly.  It
  is likely that, given a good understanding of the chipset, a driver
  can be written and debugged in a day or two.  For someone just
  learning about this kind of programming, a week is more reasonable.



  10.  Advanced Topics

  Newer chipsets are getting into two advanced areas: programmable clock
  generators, and accelerated capabilities (BitBlt, line drawing, HW
  cursor).  These are new areas, and the formal interfaces to them are
  not yet defined.  It is advised that you contact the XFree86 team and
  get involved with the development/beta-testing team if you need to be
  working in these areas.


  11.  References


     o  Programmer's Guide to the EGA and VGA Cards, 2nd ed.

        Richard Ferraro

        Addison-Wesley, 1990

        ISBN 0-201-57025-4

        (This is the bible of SVGA programming - it has a few errors, so
        watch out).

     o  vgadoc3.zip

        Finn Thoegersen

        (This is a collection of SVGA and other chipset documentation.
        It is available on most MS-DOS/Windows related FTP archives,
        including wuarchive.  It is DOS/BIOS oriented, but is still
        extremely useful, especially for developing probe functions).


  12.  Vendor Contact Information


     ATI Technologies (VGA-Wonder, Mach8, Mach32)
        33 Commerce Valley Drive East" Thornhill, Ontario

        Canada L3T 7N6

        (905) 882-2600 (sales)

        (905) 882-2626 (tech support)

        (905) 764-9404 (BBS)

        (905) 882-0546 (fax)


     Chips & Technologies
        ???


     Cirrus Logic (SVGA, Accelerators - CL-GD5426)
        3100 West Warren Ave.

        Fremont, CA  94538

        (510) 623-8300 (N. CA, USA)

        (49) 8152-40084 (Germany)

        (44) 0727-872424 (UK)

     Genoa Systems (GVGA)
        75 E. Trimble Road

        San Jose, CA 95131

        (408) 432-9090 (sales)

        (408) 432-8324 (tech support)


     Headland Technologies, Inc (Video-7 VGA 1024i, VRAM II)
        46221 Landing Parkway

        Fremont, CA  94538

        (415) 623-7857


     Oak Technology, Inc (OTI-067,OTI-077)
        139 Kifer Ct.

        Sunnyvale, CA 94086

        (408) 737-0888

        (408) 737-3838 (fax)


     S3 (911, 924, 801
        805, 928)/ (408) 980-5400


     Trident Microsystems Inc (8800, 8900, 9000)
        205 Ravendale Dr

        Mountainside, CA 94043

        (415) 691-9211


     Tseng Labs Inc,
        6 Terry Drive

        Newtown, PA  18940

        (215) 968-0502


     Weitek (Power9000, 5186)
        1060 E. Arques Ave,

        Sunnyvale, CA  94086

        (408) 738-5765


     Western Digital
        (714) 932-4900

  $XConsortium: VGADriv.sgml,v 1.3 95/01/23 15:34:51 kaleb Exp $
  Generated from XFree86: xc/programs/Xserver/hw/xfree86/doc/sgml/VGADriv.sgml,v 3.5 1995/01/28 16:02:34 dawes Exp $






$XFree86: xc/programs/Xserver/hw/xfree86/VGADriverDoc/VGADriver.Doc,v 3.13 1995/07/12 15:33:21 dawes Exp $